## Slide 1: Progress Report
Paul Ruess
Sept. 21, 2016

## Slide 2: Progress Made
USGS rating curves from URL
http://waterdata.usgs.gov/nwisweb/get_ratings?file_type=exsa&site_no={0}
HAND rating curves from netCDF file (from Xing)
Calculated HAND rating curves from netCDF file (from Xing)
  Using WetArea, HydraulicRadius, and Slope parameters with a fixed n
  Tested with n = 0.05 and is nearly identical to Xing’s rating curves
Manually approximated n-value to match HAND to USGS rating curves

## Slide 11: Summary of Results
Average n: 0.265

## Slide 12: Next Steps
Automate determination of manning’s roughness for each COMID, given USGS rating curve data.
Compare automated to manual results and adjust accordingly.
Iterate until automation is relatively correct.

## Slide 13
“INDEP” = Height (ft)
“SHIFT” = displacement from actual bottom
( subtract from INDEP to get actual)
“DEP” = Discharge(cfs)

## Slide 14
“INDEP” = Height (ft)
“DEP” = Discharge(cfs)
“INDEP” = Height (ft)
For each COMID:
  For each height (ft) in HAND netCDF file (0, 1, 2, … 48)
    Pull corresponding WetArea, HydraulicRadius, and Slope
    Pull corresponding USGS discharge (use USGS rating curve)
    Calculate manning’s roughness
  Average all roughness values together
Return average manning’s roughness for each COMID

## Slide 15: At-a-station Hydraulic-Geometry (AHG)
Use river geometry to determine stream velocity
U = velocity
K = 1 / n , n = manning roughness
Y = average channel depth
S = slope
P = 0.667 (Dingman, 2007)
Q = 0.500 (Dingman, 2007)

## Slide 16: AHG continued
Y = average depth
Ym = maximum depth
r = shape of channel (2 for parabolic)
Given Ym, can compute Y given r

## Slide 17: AHG continued
Can then use following relationships to calculate a, b, c, f, k, m
Finally, plug Q into manning’s equation using HAND WetArea, HydraulicRadius, and Slope, and back-calculate roughness.

## Slide 18: Final Plan
Define machine-learning algorithm to compute manning’s roughness using a fraction of available USGS rating curve data (ie. 90%)
Manually assign roughness to test fraction (ie. 10%)
Apply algorithm to test fraction (ie. 10%)
Validate/verify correctness of algorithm on test fraction (ie. 10%)
Compare automated to manual results and adjust accordingly.
Implement algorithm on remaining 2.7 million reaches